## Slide 1: Finding Shear Modulus With A Torsional Experiment
By: Evan Galloway, Alex Huynh, Dale Loveland, Tyson Patterson
ME321: Measurement Systems
1/16/2026
Notes: - Speaking evan
()
- YOU HAVE A MAX OF 1 MIN PER SLIDE

## Slide 2: A torsional beam tester was used to find the shear modulus of a metal rod.
Force ()
Deflection Angle()
Disc Radius (
Rod Length ()
Rod Radius ()
1
2
3
Notes: Speaking
(Person 1)
Go from left to right
From top to bottom
Explain how each one is a measurand and how the symbols are used to refer to each one in the project

## Slide 3: The following procedure was used to collect the experimental data.
Measured the length and diameter of the metal testing rod
Measured diameter of disc and recorded the zero balance
Applied a controlled constant force of 4.4 lbf by hanging the weight as seen in the previous diagram
Recorded the angular displacement in degrees and compensated for the zero balance
Repeated Steps 3 and 4 for 8 total trials
Notes: Speak
Person 2
Don’t explain too much since you should mostly explain this on the slide before
Maybe go into the zero balance a bit
Mention how step five was not completed until a shakedown had been done and validated

## Slide 4: We started with a shear modulus equation that fit our apparatus to derive our Data Reduction Equation to fit with our measurands.
G : Shear modulus
τ : torque applied to the rod
L : length of the rod
J : polar moment of inertia of a cylinder
θ : angular displacement
Notes: (Person 2) Potentially add in another picture of our apparatus
Mention how this is from statics 2 and how this equation is actually derived from another one
We are implying that we derived our DRE to fit our measurands

## Slide 5: After recording a value for each measurand from the data reduction equation, a resultant was found for shear modulus.
Parameter | Value
 | *
 | 3.77
Parameter | Value
*Degrees were converted to radians for this calculation
Notes: Person 1
Quick slide that can mention our shakedown values and systematic uncertainty resultant

## Slide 6: The relative systematic uncertainty was found to be reasonable enough to proceed with multiple measurements.
Notes: Person 1
- Explain how this was just under the 5% standard so we felt it was appropriate to conduct more trials

## Slide 7: After 8 trials, multiple different deflection angles (deg) were measured to find the random uncertainty.
Observation | (Radians) | (Degrees) | Shear Modulus (psi)
1 | 0.148 | 8.50 | 3.32
2 | 0.131 | 7.50 | 3.77
3 | 0.133 | 7.60 | 3.72
4 | 0.134 | 7.70 | 3.67
5 | 0.140 | 8.00 | 3.53
6 | 0.145 | 8.30 | 3.40
7 | 0.131 | 7.50 | 3.77
8 | 0.133 | 7.60 | 3.72
Average | 0.137 | 7.93 | 3.61
Std Dev | 0.006 | 0.37 | 0.18
Observation |  |  | Shear Modulus (psi)
1 | 0.148 | 8.50 | 
2 | 0.131 | 7.50 | 
3 | 0.133 | 7.60 | 
4 | 0.134 | 7.70 | 
5 | 0.140 | 8.00 | 
6 | 0.145 | 8.30 | 
7 | 0.131 | 7.50 | 
8 | 0.133 | 7.60 | 
Average | 0.137 | 7.93 | 
Std Dev | 0.006 | 0.37 | 
Chart: Trial Number
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 8.5 | 7.7 | 7.6 | 7.5 | 8.3 | 8 | 7.5 | 7.6
Trendline | 7.84 | 7.84 | 7.84 | 7.84 | 7.84 | 7.84 | 7.84 | 7.84
Notes: Person 2
- Hit on the graphic and standard deviation

## Slide 8: After collecting the results from multiple trials, the random uncertainty was calculated.
: critical t-value
: Standard Deviation of G
: number of trials
Notes: Person 2
- Quick slide to show how random was calculated
With a t-value of 2.365, the standard deviation of G from the previous slide, and for 8 trials, we calculated the random uncertainty.

## Slide 9: The deflection angle and random were the greatest sources of uncertainty.
Parameter | Representative Value | Uncertainty | Sensor | Sensitivity Co | )
 | 7.9 (deg) |  | Tick Marks |  | 
 | - | - | - | - | 
 | 0.19 (in) |  | Calipers |  | 
 | 4.4 (lbf) |  | Scale |  | 
 | 45.18 (in) |  | Ruler |  | 
 | 4.915 (in) |  | Calipers |  | 
 | 3.61x (psi) | - | - | - | 
Parameter | Representative Value | Uncertainty | Sensor | Sensitivity Co | 
 | 7.9 (deg) |  | Tick Marks |  | 
 | - | - | - | - | 
 | 0.19 (in) |  | Calipers |  | 
 | 4.4 (lbf) |  | Scale |  | 
 | 45.18 (in) |  | Ruler |  | 
 | 4.915 (in) |  | Calipers |  | 
 |  | - | - | - | 
Notes: Person 2
Make sure to mention theta and random for sure
Mention that the disc had an insignificant role in the total uncertainty

## Slide 10: After taking multiple trials and accounting for the random uncertainty, the total relative uncertainty was calculated and divided by the shear modulus.
Notes: Person 1
Expected it to be higher as we added a lot of random uncertainty
Feel it was appropriate still and get ready to show why with out conclusion

## Slide 11: We concluded with the total relative uncertainty deemed appropriate, that the shear modulus of the rod is .
We recommend using a more precise way to measure the deflection angle to lower uncertainty.
Notes: Person 2
- Deflection angle had the worst sensor to it, which would help a lower random and systematic uncertainty if it were better

## Slide 12: The End
Questions?

## Slide 13: Q/A Slides
First Shakedown Attempt
Uncertainty Tree
Calibration of Weight Scale
Apparatus Breakdown
Sensitivity Coefficients
Specific Aluminum Alloy
DRE Derivation
Notes: “Back-Up” Slide with links

## Slide 14
Parameter | Typical Value | Uncertainty | Units | WX | WG
 | 0.239 |  | In |  | 
 | 7.5 |  | deg |  | 
 | 45.18 |  | in |  | 
 | 4.4 |  | lbf |  | 
 | 5.063 |  | in |  | 
G | 3.96x | - | psi | - | 
Parameter | Typical Value | Uncertainty | Units | WX | WG
 | 0.239 |  | In |  | 
 | 7.5 |  | deg |  | 
 | 45.18 |  | in |  | 
 | 4.4 |  | lbf |  | 
 | 5.063 |  | in |  | 
G |  | - | psi | - | 
Our values from our first shakedown attempt before switching to calipers.
Back
Notes: Need to put partial dif
Add link

## Slide 15: This is our systematic relative uncertainty before switching to calipers to measure the rod radius.
Back
Notes: - Tie in shear modulus equation at the bottom to show how a systematic uncertainty in the rod radius propagates so far

## Slide 16: Uncertainty Tree
WG
0.23x106 psi
Wr,rod
0.05x106 psi
WL,rod
0.004x106 psi
Wr,Disc
<0.001x106 psi
Wθ
0.16x106 psi
WG,rand
0.15x105 psi
WF
0.004x106 psi
WG,sys
0.17x106 psi
Back
Notes: Add link

## Slide 17: Sensitivity Coefficients (Partial Derivatives)
Back

## Slide 18: 6061 Aluminum was the closest specific aluminum alloy that could be found.
*McMaster-Carr
**Matweb
Calculated Shear Modulus:
We found that Aluminum rods are commonly made using 6061 Aluminum*
From Matweb* 6061-T6 Datasheet:
Back

## Slide 19: Calibration of weight scale used to find accuracy.
Chart: Scale Calibration
| 0.01 | 0.02 | 0.05 | 0.1 | 0.5 | 1 | 2 | 3 | 3.5 | 4.5 | 4.9000000000000004
 | 0.025 | 0.04 | 0.11 | 0.215 | 1.1 | 2.205 | 4.41 | 6.61 | 7.71 | 9.915 | 10.8
Back
Notes: Add link

## Slide 20: Steps to derive the Shear Modulus Equation used for our DRE.
Back
 | (1)
 | (2)
 | (3)
 | (1)
 | (2)
 | (3)
: Shear Stress
: Shear Strain
DRE
*
* Small-angle approximation assumed
Notes: Tau/J is just F/A
Tan(theta)/L is just change in length over original length
You can explain this and just mention its circular instead of square

## Slide 21: Hang a known mass off the disk
Force ()
Back
Notes: link

## Slide 22: Use a disk with tick marks to measure the degree change.
Disk Reading (deg)
Back

## Slide 23: Measure the radius of the disk for the use in the Shear Modulus equation
Disk Radius (in)
Back

## Slide 24: Measure the rod length to include it as a measurand.
Rod Length (in)
Back

## Slide 25: Measure the rod radius with calipers for the equation.
Rod Radius (in)
Back

## Slide 26: Sources
https://www.researchgate.net/publication/334465619_MATERIALS_SCIENCE_AND_ENGINEERING
https://www.xometry.com/resources/3d-printing/what-is-shear-modulus